## Slide 1: Compost Workshop Estonia - 6 October 2017
COMPOSTING and COMPOST QUALITY – How to manage – how to achieve – how to evaluate?
Florian Amlinger Compost – Consulting & Development 100NGO

## Slide 2: Draft EU FertReg - Compost / Digestate Quality Criteria
 | SOLID ORG. FERTILISER [compost] |  | SOIL IMPROVER [compost] | LIQUID ORG. FERTILISER [digestate]
Dry matter % Fresh Matter | > 40% |  |  | < 40%
N total % Fresh Matter | ≥ 2.5 % |  | ---. | ≥ 2 %
P2O5 total % Fresh Matter | ≥ 2% |  | --- | ≥ 1%
K2O total % Fresh Matter | ≥ 2% |  | --- | ≥ 2%
Org. CARBON % Fresh Matter | ≥ 15% |  | ≥ 7.5% | ≥ 5%
Stability |  |  |  | 
OXIGEN UPTAKE RATE mmol O2/kg organic matter/h | ≤ 25 mmol |  |  | ≤ 50 mmol
SELF HEATING FACTOR | Rottegrad III (40 - 50 °C) |  |  | ---
Residual Biogas Potential Litre biogas / g volatile solids | --- | --- |  | 0,45 l biogas

## Slide 3: Draft EU FertReg - Compost / Digestate Quality Criteria
 | SOLID ORG. FERTILISER [compost] | SOIL IMPROVER [compost] |  | LIQUID ORG. FERTILISER [digestate]
Cd (mg/kg d.m.) | 1.5 | 3 (+ growing medium) |  | 1.5
Cr (mg/kg d.m.) | CrVI: 2 |  |  | 
Hg (mg/kg d.m.) | 1 |  |  | 
Ni (mg/kg d.m.) | 50 (growing medium: 100) |  |  | 
Pb (mg/kg d.m.) | 120 (growing medium: 150) |  |  | 
Cu (mg/kg d.m.) | DECLARE ABOVE 200 mg |  |  | 
Zn (mg/kg d.m.) | DECLARE ABOVE 600 mg |  |  | 
PAH16* (mg/kg d.m.) | 6 |  |  | 
Biuret (C2H5N3O2) (g/kg d.m.) | 12 |  | --- | 12
Salmonellae | ABSENT in 25 g |  |  | 
E. coli OR Entercoccaceae | < 1000 CFU/g fresh mass |  |  | 
Impurities (glass, metal, plastics) in > 2 mm (% d.m.) | NOW: < 0,5 % AFTER 8 YEARS: < 0,25 % |  |  | 

## Slide 4: „Maturity“ / „Stability“ Criteria for COMPOST
Example from VLACO/BE – Wim Van den Auweele
Based on historical dataset of Flemish compost samples, the correlation between the SHT (Rottegrad, determined at 22 ± 2 °C) and the OUR (determined at 20 ± 2 °C) is:

## Slide 5: Plant Response
 growing media, bagged … 25% compost  > 95% biomass  private gardening 50% compost  > 90% biomass relative to standard substrate Cress (Lepidium sativum) & Chinese cabbage (Brassica rapa ssp chinensis)
OPEN & CLOSED CRESS TEST:
  Fully mature Compost  100% performance in both tests

## Slide 6: Minimum STANDARDS for Open Windrow composting
Minimum bulky/structure material
  BIO-WASTE
    Bulk density Bio-waste URBAN: ~ 0,75 t/m³.
    Bulk density Bio-waste RURAL: ~ 0,5 t/m³
    Volume reduction composting: ca. ~ 40 – 70 %
Origin of Bio-waste | Min % shredded wood per year | By Volume (v/v)
RURAL | 15% + oversize screenings | 1 : 0,5
URBAN | 25% + oversize screenings | 1 : 1
Type of structure material | Min % structure material By MASS | By VOLUME
STRAW | 20% | 1 : 2,5 – 3
SHREDDED WOOD | 30% | 1 : 1,5 – 2
  SEWAGE SLUDGE
    Bulk density shredded wood: 0,25 - 0,35 t/m³.
    Bulk density Sewage sludge: 0,8 – 1,0 t/m³
    Volume reduction composting: ca. ~ 50 %
Notes: Excogenic means „External“

## Slide 7: Minimum STANDARDS for Open Windrow composting Windrow Size & Turning Frequency
Height | Cross Section | Width | Turnings/ week | Minimum total rotting time | 
 |  |  |  | Bio-Waste | Sewage Sludge
< 1,5 m | 3 m³/m | 3 m | 2 -5 | 7 | 8
 |  |  | 1 | 8 | 10
1,5 – 1,8 m | 3 - 4 m³/m | 3,5 m | 2-5 | 8 | 9
 |  |  | 1 | 10 | 12
1,8 – 2,2 m | 4 - 6 m³/m | 4,5 m | 2-5 | 9 | 10
 |  |  | 1 | only with aeration | only with aeration
2,2 – 2,5 m | 6 - 7,5 m³/m | 5 m | 2-5 | 10 | only with aeration
 |  |  | 1 | only with aeration | only with aeration
BIO-WASTE & SEWAGE SLUDGE Composting

## Slide 8: AT Compost Ordinance / Quality Criteria: LIMIT Values
 | Class A+ ORGANIC FARMING | Class A ALL / GENERAL FARMING | Class B NON FOOD
Compost from SOURCE SEPARATED BIO-WASTE |  |  | 
Cd (mg/kg d.m.) | 0.7 | 1 | 3
Cr (CrVI) (mg/kg d.m.) | 70 (0) | 70 | 250
Hg (mg/kg d.m.) | 0.4 | 0.7 | 3
Ni (mg/kg d.m.) | 25 | 60 | 100
Pb (mg/kg d.m.) | 45 | 120 | 200
Cu (mg/kg d.m.) | 70 | 150 | 500 (400)*
Zn (mg/kg d.m.) | 200 | 500 | 1800 (1200)*
MIXED WASTE Compost additionally: |  |  | 
PAH16* (mg/kg d.m.) | -- | -- | 6
AOX (mg/kg d.m.) | -- | -- | 500
Oil based HC (mg/kg d.m.) | -- | -- | 3000
PCB (mg/kg d.m.) | -- | -- | 1
Dioxin (ng Teq/kg d.m.) | -- | -- | 50
* Declaration threshold Cu = 400 mg // / Zn = 1200 mg

## Slide 9
AT Compost Ordinance USE RELATED Quality Criteria | GROWING MEDIA / priv.GARDENING / in BAGS | FARMING | Landscaping | Landfill Reclamatioln
Org. Matter (% d.m.) | > 20 | > 20 | > 20 | > 20
El. Conductivity (mS/cm) | ≤ 3 | -- | -- | --
Max. particle size (mm) | 40 | 40 | 40 | 40
Σ Impurities >2 mm (% d.m.) | 0.5 | 0.5 | 1.0 | 1.0
Plastics >2 mm (% d.m.) | 0.2 | 0.2 | 0.4 | 0.4
Plastics >20 mm (% d.m.) | 0.02 | 0.02 | 0.04 | 0.04
Metals (% d.m.) | 0.2 | 0.2 | -- | --
Glas (% d.m.) | 0.2 | 0.2 | -- | --
Growth Test with “CRESS” [Lipidium sativum] | Biomass [% of standard substrate] | -- | -- | --
25 Vol-% compost: |  |  |  | 
 | > 95% | -- | -- | --
50 Vol-% compost: | > 90% | -- | -- | --
Viable seeds / weeds | ≤ 3 / litre | -- | -- | --
Salmonellae | none | none | none | none
Pathogenic E.coli | none | none | None in play / sport grounds | --
Campylobacter | none | -- | -- | --
Listeria sp. | none | -- | -- | --

## Slide 10: Kompostimise õppepäev: … kuidas mõista komposti kvaliteeti?
Quick tests for practice and learning
NO2 0
NO3 200 – 300 mg/kg
NH4 <2 mg/kg
pH actual (in H2O) 7 – 8
pH potential (in 1 N KCl) 7 – 8
Difference pH act. – pH pot. < 0,3
Sulfid 0
El. Conductivity < 3 mS /cm
Cress Test positive !
Additional Laboratory tests and requirements
Organic matter 20 – 35 % d.m.
Impurities < 0,5% d.m.
Heavy metal limits for agricultural use
Salmonella: 0
Pathogenic E. Coli 0
> 55 °C for 10 days and 2 – 3 turnings
Criteria for the „Komposkar“
Award

## Slide 11: FLEXIBLE Time –Temperature profile for composting – as required e.g. in Austria
https://www.bmlfuw.gv.at/greentec/abfall-ressourcen/behandlung-verwertung/behandlung-biotechnisch/richtlinie_sdt.html

## Slide 12
The controlled process: °C & CO2
oC & CO2 in a controlled process
CO2
oC
Temperature max. 60-65 °C
Sufficient OXIGEN min. 5 (1)%
Maximum CO2 max. 10 – 15 %

## Slide 13: Use of ABP in Biogas/Compost (roughly separated into 4 groups)
Catering waste (Cat.3),
former foodstuff
Manure, DT-Content (Cat.2), milk & milk products; bio-waste without catering waste
No specific pre-treatment required! (Exemption: Suspect of infectious diseases)
National rules are applicable;
-> Products may only be placed on the market within MS !
Other Cat.2-Material
i.e. parts of inedible animals
Other Cat.3-Material
i.e. slaughter waste, blood, fat, feathers, bristles, etc.
Pressure sterilisation (‚Method 1‘) - beforehand in an approved rendering plant
EU-standard parameters apply
(70°C, 60 min, 12 mm)
or Validated Process
Required treatment:
Possible input material:

## Slide 14: National Implementation of the ABPR
ABP-Regulation (EC) 1069/2009
  National rules for catering waste (households, restaurants)
  OPEN WINDROW Composting  OK
    … if all the material in the system is exposed over the required time to a defined temperature level  TURNING  MONITORING
Notes: Excogenic means „External“

## Slide 15
Member States may adopt or maintain national rules for:
  CATERING WASTE
    Food waste from central and household kitchens
  manure;
  digestive tract content separated from the digestive tract;
  milk; milk-based products; milk-derived products; colostrum; colostrum products;
  eggs; egg products;
  Processed former food stuff
CATERING WASTE ….  National rules

## Slide 16
Processing requirements COMPOSTING:
  CATERING WASTE from HOUHEHOLDS
    Mixing and treatment within 24 hours after tipping with suitable bulking agents in order to initiate an effective composting
  CATERING WASTE from CENTRAL KITCHENS / processed former foodstuff
    Mixing and treatment immediately after tipping with suitable bulking agents in order to initiate an effective composting
    Covering the windrows with fresh or mature compost, shredded material or geo-textiles (com-post fleece) throughout the thermal sanitisation period (~ 10 to 14 days)
CATERING WASTE ….  National rules

## Slide 17: Treatment of Catering Waste in Biogas Plants
Possible options according to Austrian ABP-Ordinance as no BAT for such treatment available for biogas-plant:
  Fermentation as thermophilic process at  55 °C with
  20 d retention time; particle size  12 mm or
  Mesophilic fermentation combined with pasteurisation
    Temperature  70 °C for 1 h, particle size  12 mm or
    Temperature  60 °C for 5 h, particle size  12 mm or
  Composting of fermentation-residues according to national standards (BAT, see above)

## Slide 18: Hygiene Aspects in Process Management
Further Measures & Records (as part of the QM)
  watering, turning, aeration, material additions, screening…
& …… separating / working from DIRTY to CLEAN zone
Delivery/tipping of Bio-waste
Intensive Composting Hygienisation Phase
MATURATION Phase
Ready made COMPOST STORAGE
Foto: Courtesy of Seiringer Umwelttechchnik GmbH

## Slide 19
2.5 to 5 % slope
Sealed /paved surface for the main rotting area draining of rain and waste water

## Slide 20
Composition
40 % shredded bush and tree cuttings
30% fine garden waste
10% rotted cattle manure
10% loamy soil
Composting
8 to 12 weeks (summer)
12 to 20 weeks (winter)
Turning : 5 to 3x/week
Screening: 10 to 20 mm
ON-FARM FIELD COMPOSTING

## Slide 21: International QAS for compost http://eu100ngo.net/qas/
provided by: “100 NGO” / “Compost & Biogas Association Austria Austria”

## Slide 22
Many Thanks!
Florian Amlinger
eu100ngo@gmail.com
www.eu100ngo.net
Notes: As the Draft Directive on Biological Treatment mandates source separation to be implemented also in towns, I want to show that purity of sorted waste depends not so much on the size of the population; it is linked to the type of scheme, instead.