## Slide 1: INTERREG Meeting ATCZ-86
WaterMon
19.01.2021

## Slide 2: Project Management

## Slide 3: Report Periods
Nr. der Berichtsperiode / Pořadové číslo monitorovacího období | Beginn der Berichtsperiode / Začátek monitorovacího období | Ende der Berichtsperiode / Konec monitorovacího období | Art des Projektberichts / Druh Zprávy o projektu
0 | 01.06.2019 | 31.12.2019 | Zwischenbericht_Průběžná
1 | 01.01.2020 | 31.12.2020 | Zwischenbericht_Průběžná
2 | 01.01.2021 | 31.12.2021 | Zwischenbericht_Průběžná
3 | 01.01.2022 | 31.12.2022 | Endbericht_Závěrečná
4 |  |  | 
5 |  |  | 
6 |  |  | 

## Slide 4: Parameters
Physical, chemical parameters
  DUK: COD, BOD, DOM, Temperature, Nitrate, Nitrite, BIX, FIX, Oil film
  CEITEC-VUT: Phosphorus, Ammonia, Uranium
Microbiological parameters
  CEITEC-VUT: e-coli
  DUK: e.g. Cyanobacteria (cyanotoxins - microcystin…)

## Slide 5: Monitoring-Station Concept
Power supply
Sensors DUK
Sensors CEITEC
Control unit
Wireless interface
Solar panel, Battery
Open Points:
Supply voltage, power consumption - power management
Interfaces - bus protocol
Overall size, module size
Security protection (data protection, stealing of station)
Buoy or stationary station
Notes: Power should supplied by a solar panel

## Slide 6: System architecture
Colorimetric sensor
(DUK)
Electrochem. sensor
(MENDELU)
Optical sensor
(DUK)
Power Management
(CEITEC)
CPU
(DUK)
Data interface
(DUK)
Power control
(CEITEC)
GSM
(DUK)
Memory
Solar Panel
Battery
Pump
Reagent
Buffer
Colorimetric sensor
(BUT)
Reagent
River water inlet
Water outlet
Waste reservoir
Waste outlet
Data server
(DUK)
Filter
IMU
Reservoir

## Slide 7: Colorimetric device concept
Power consumption:
defined mainly by pumps
Size:
due to microfluidic could be cartridge size – easily exchangeable

## Slide 8: Solution for multi-colorimetric analysis
•We can make join platform for sample distribution
•Microfluidic system assure very low consumption of reagent and low waste

## Slide 9: Power Supply
Power supply by solar panel
  Design: Power consumption by modules?
  Main supply voltage: 12V/DC
  Sampling period: 1/week, on request, (max.1/Dy)
  1 common pump for all modules open
  VUT: 5V, 1A max - Wh according to sampling
  Ceitec: 2x per day for 30 minuts, we need 5V 500mA - 2.5Wh for e-Coli
  DUK: Module 30x30x30cm, 30min, 2Amax, 5V
  cooling of the device, ventilation

## Slide 10: Communication
Protocol for communication between the modules
  5V RX/TX UART protocol
Communication station <-> database
  GSM
GPS Module
  for safety reasons

## Slide 11: Control Board
Stand alone sensor modules (uC & pump on board)
Control board collect data
  main pump
  data transfer to/from data base
  Offline data (raw data) storage (e.g. SD-card)
  e.g. software update via SD-Card
  GPS position, alarm if position is changed
  alarm if parameters out of range (Temp, moisture, voltage…)
Power management
  Solar pannel
  Battery
  Power scheduler
  Fan, air condition
  Status lights

## Slide 12: Webserver & Webpage
Water Quality
Sensor
Y
Webserver
Y
GSM Data Transfer
Webpage
User
Authorization
required
River
Antenna
Antenna

## Slide 13: Suggestions
Sensor modules 3x
Reservoir for immediate samping based on GMS request

## Slide 14: Publicity
There is a database (iBox) on the program website (www.at-cz.eu), which serves as each project's own website. The lead partner is obliged to update the iBox regularly (at least once per reporting period) with evidence of activities undertaken, outputs and results achieved, and information and publicity measures. Access data will be provided to the lead partner only upon conclusion of the ERDF funding contract.
Each project partner is obliged to display a poster (minimum size A3) with the program logo and information about the project, indicating the financial support provided by the program, in a suitable, clearly visible place accessible to the public throughout the project duration.
Roll up pannel
The program logo must be used for all information and communication measures with which a project partner approaches the public (printed materials, audiovisual materials, lists of participants, etc.).
Download on Website

## Slide 15: Project Plan (DUK)

## Slide 16: ToDo’s
Date | Subject | Who | Until | Done | Comment
19.01.21 | Half-year meeting | MB | W4 |  | 
 | Reporting in iBox (every reporting period) | MB | W9 |  | 
 | Project Poster A3 | MB | W4 |  |