## Slide 1: INTERREG Meeting ATCZ-86
WaterMon
04.11.2021
Thomas Posnicek (DUK)
DOM-SAC Sensor Module

## Slide 2: Overview
What’s the aim
The Measuring principle
Sensor Module
Next steps

## Slide 3: The Aim
A compact Sensor Module to measure the following paramters…
        DOM (dissolved organic matter)
        SAC (spectral absorption coefficient)
        COD (chemical oxygen demand)
        BOD5 (biochemical oxygen demand)
…in an optical way.

## Slide 4: Measuring principle
DOM
(dissolved organic matter )
calculate
  BIX
  (biological-index)
  FIX
  (fluorescence-index)
Ex. 310nm
Em. 380nm
Em. 430nm
Ex. 370nm
Em. 450nm
Em. 500nm
Fluorescence measurement
calculated on two
fluorescence indices
SAC
(spectral absorption coefficients)
254nm
  COD and BOD5
(chemical oxygen demand & biochemical oxygen demand)
Absorbance measurement
435nm
550nm

## Slide 5: Sensor Modul for DOM & SAC
BIX and FIX?
are optical indices
significant relationship with molecular formulas
characterize the DOM composition and its origin
BIX indicator of autotrophic production
FIX distinguish DOM derived from terrestrial sources vs. microbial sources

## Slide 6: Sensor Modul for DOM & SAC

## Slide 7: Sensor Modul for DOM & SAC

## Slide 8: Preliminary results
DOM
SAC
comparative measurement of KHP (potassium hydrogen phthalate, C8H5KO4) with literature reference DIN-standard 38404-3 and our system
measurements of different DPH (fluorescent hydrocarbon - Diphenylhexatriene, 1,6-Diphenyl-1,3,5-hexatriene) concentrations with our system compared to the fluorescence spectrometer LS55 (PerkinElmer, USA)

## Slide 9: Next Steps
Verification of the module
Construction of a second and third module
Implementation in the overall system

## Slide 10: Thank you for the Attention