## Slide 1: INTERREG Meeting ATCZ-86 Krems
WaterMon
04.11.2021

## Slide 2: Spectrophotometric detection of phosphorus
Atripan Mukherjee

## Slide 3: Outline
Literature study
Preliminary study for phosphorus detection.
Reagent stability
Temperature stability
Conclusion

## Slide 4: Sample preparation
Solution A: 1.5 g of Antimony potassium tartrate was dissolved in 20 mL milli-Q water containing 2.5 mL of sulphuric acid. And it was diluted to 25 mL.
Reagent: 6.25 mL of solution A was added to 25 sodium molybdate (0.52 M) solution containing 0.2 g ascorbic acid.
Reagent
Solution A
Eisenreich, S.J., Bannerman, R.T. and Armstrong, D.E., 1975. A simplified phosphorus analysis technique. Environmental letters, 9(1), pp.43-53.
Incubation 30 min
Phosphorus sample
+ reagent

## Slide 5: Measurement
The initial absorbance spectra was 880 nm, later recommended to 550-700 nm.
So, protocol was revised by optimising amount of colouring reagent and measured at 650 nm.
The reagent stability study was done at different temperature condition.
1 day
45 day
30 day

## Slide 6: Reagent stability
1 day
45 day
30 day

## Slide 7: Results and Calibration
Sensitivity remains almost same with decreasing reagent concentration
At 4°C, reagent is found to be more stable.

## Slide 8: Conclusion
0.3 mL of reagent were required (min.) for total 2 mL volume.
Reagent is found to be sensitive for a month, following 35 days decolouration of reagent occur from colourless to pale yellow.
The reagent needs to be kept at 4 °C for longer stability and sensitivity.
EU recommended 0.05mg/L in water

## Slide 9: Thank you for the Attention Questions ?